## Slide 1
Conway game of life
Filippova Daria 24216
Muruev Denis 24216
Vilegzhanin Maksim 24216

## Slide 2
Create a workable model of Conway Game of Life game combining hardware and software using CDM-8e
Goal
Filippova Daria 24216
Muruev Denis 24216
Vilegzhanin Maksim 24216

## Slide 3
Classic rules of the
Game of life
If there are 3 or more living cells near to dead cell it comes to life.

## Slide 4
Classic rules of the
Game of life
If there are 2 or 3 living cells near a living cell, the cell continues to live. Otherwise, the living cell dies

## Slide 5
Project extensions
Parameterized birth/survival conditions
Two modes: “creative” (fixed field) and “survival” (zone shrinking).

## Slide 6
Project extensions
Parameterized birth/survival conditions
Two modes: “creative” (fixed field) and “survival” (zone shrinking).
Creative
Survival
Game modes:

## Slide 7
Project extensions
Also added the ability to set one on of the 8 ready-made deferent patterns
HARDWARE

## Slide 8
Hardware
Main sсheme
combines all parts of the circuit together
HARDWARE

## Slide 9
Hardware
Change X cell in the current Y row to the opposite and sends the result row to write buffer
converter

## Slide 10
Hardware
Change X cell in the current Y row to the opposite and sends the result row to write buffer
converter

## Slide 11
Hardware
Change X cell in the current Y row to the opposite and sends the result row to write buffer
converter

## Slide 12
Hardware
buffers
There are two field states. one can be edited in the Write buffer. The other is static in the Fixed buffer.
Write
Fixed

## Slide 13
Hardware
buffers
There are two field states. one can be edited in the Write buffer. The other is static in the Fixed buffer.
Write
Fixed
Contains 32 registers for recording input row, also masks for shrinking the field horizontally and tunnels with OR gate for shrinking vertically
horizontally
vertically
input row
Write
buffer

## Slide 14
Hardware
buffers
There are two field states. one can be edited in the Write buffer. The other is static in the Fixed buffer.
Write
Fixed
Just contains 32 registers for recording new state of field from write buffer
Fixed
buffer

## Slide 15
Hardware
buffers
There are two field states. one can be edited in the Write buffer. The other is static in the Fixed buffer.
Write
Fixed

## Slide 16
Hardware
neighbor module
It gives the number of neighbors, the cell state and the flag that the row is completely empty

## Slide 17
Hardware
neighbor module
It gives the number of neighbors, the cell state and the flag that the row is completely empty
Takes 3 rows Y, Y-1, Y+1 and counts the number of neighbors near cell X Y. If all three rows are empty, the flag for skipping this row Y is raised.
Y
Y-1
Y+1
number of neighbors
Flag

## Slide 18
Hardware
neighbor module
It gives the number of neighbors, the cell state and the flag that the row is completely empty
This scheme also uses modules to get the state of cell X from row

## Slide 19
Hardware
neighbor module
It gives the number of neighbors, the cell state and the flag that the row is completely empty

## Slide 20
Hardware
survival module
Indicates victory or defeat in survival mode

## Slide 21
Hardware
Visualization modules
Vizualize cursor and shrinking zones on the matrix

## Slide 22
Hardware
Status bar
shows the current state of the game:
WIN
LOSE
SIMULATION
EDIT
I/O

## Slide 23
Hardware
There are a total of 17 IO devices. Let’s see the important ones
I/O

## Slide 24
Hardware
These devices store the current X and Y that the CPU is processing now.

## Slide 25
Hardware
And also, a device that stores game states (ON/OFF). The CPU and the User can change this game state
SOFTWARE

## Slide 26
Software
There are also 17 I/O interfaces that have the same names as in the schematic.
Tables of conditions
I/O interfaces
SOFTWARE

## Slide 27
Software
There are 8-bit byte birth and death condition tables for a quick check of the cell.
8 because the neighbors of the cell are 8
Tables of conditions
I/O interfaces

## Slide 28
Software
Separately added survival condition with 0 number of neighbors
Tables of conditions
I/O interfaces

## Slide 29
Labels referring to functions
Loading Condition
Splits an 8-bit string of condition into 8 separate bytes in order by survival or death label

## Slide 30
Computing Cell
Determines whether to change the state of the current cell using condition tables
Labels referring to functions
skip dead and null-neighbors cells

## Slide 31
Computing Cell
Labels referring to functions
separate check if no neighbors near the live cell
Determines whether to change the state of the current cell using condition tables

## Slide 32
Computing Cell
Labels referring to functions
Else using condition tables
Determines whether to change the state of the current cell using condition tables

## Slide 33
Computing Cell
Labels referring to functions
After that change or not the cell state
Determines whether to change the state of the current cell using condition tables

## Slide 34
Main code
At the beginning, using the loop, we wait for the game start or for the button to draw a pattern to be pressed
Waiting for the start

## Slide 35
Main code
After startup, we load the survival and death conditions using loading Condition function
The conditions of death are produced by negating the condition of survival.

## Slide 36
Main code
If the mode is creative, the field boundaries are loaded from 0 to 31, if the mode is survival, the boundaries start from 1 to 30 and shrinking each generation
minBound
maxBound
These labels are used to limit the field to be calculated

## Slide 37
Main code
minBound - upper left border of field
maxBound - lower right border of field
minBound
maxBound

## Slide 38
Main code
loops through Y
loops through X
2 nested loops to search all cells from minbound to maxbound, it also calls the computing cell function for each cell or skip null rows

## Slide 39
Patterns
All patterns in the game are recorded as labels of this type. There are also pattern labels in the game such as:
Glider
Blinker
Butterfly
Byflops5
Monogram
mickeyMouse
Unix
QueenBee

## Slide 40
CPU takes the current position of the cursor and based on it starts to move it and draw the pattern
Patterns

## Slide 41
CPU takes the current position of the cursor and based on it starts to move it and draw the pattern
Let’s Play

## Slide 42
Thank you for listening!
Conway game of life